## Slide 1
Cooling time through a flat plate
Which method predicts the hottest-point threshold accurately at the lowest measured cost?
Synthetic input | Baseline | Units
Full thickness L | 0.010 | m
Thermal diffusivity | 1.0 × 10⁻⁵ | m²/s
Initial / face / target | 100 / 20 / 40 | °C
Outputs
Temperature profiles
Hottest-point cooling curve
First threshold-crossing time
Ideal controlled face temperatures and constant properties. Preliminary numerical study.
Notes: Timing: 0:00–0:40.
Spoken explanation:
This study asks how accurately and efficiently two numerical methods can predict the cooling of an idealised plate. The plate starts at 100 degrees Celsius inside, while both faces remain at 20 degrees. The target is when the hottest point reaches 40 degrees. The full thickness is ten millimetres and diffusivity is an illustrative ten to the minus five square metres per second. The output is a temperature field and a cooling time. These synthetic inputs support a controlled numerical comparison. A real cooling process needs justified properties and boundary data.
Sources: results/summary.json (plate and intended numerical output); configs/; docs/data_provenance.md. Engineering assumptions: docs/engineering_derivation.md. Original project brief pp. 4 and 8 require primary input/output specification.

## Slide 2
Explicit and implicit finite differences
Heat equation: T_t = alpha T_xx
FTCS | Backward Euler
Update from the old field | Solve a tridiagonal system
r = alpha dt / dx² ≤ 0.5 | Stable for any positive step
First order in time | First order in time
Second order in space | Second order in space
Accuracy still limits the implicit time step
One-dimensional conduction. Equal fixed face temperatures. No heat source, phase change or convection model.
Notes: Timing: 0:40–1:20.
Spoken explanation:
The governing equation describes heat diffusion in one direction. FTCS calculates every new interior temperature from the previous field. Its diffusion number combines diffusivity, step duration and squared grid spacing. The normal explicit runs enforce a limit of one half. Backward Euler instead uses the new field and solves a tridiagonal linear system. Known face temperatures enter the right-hand side with positive signs. Both methods have first-order time and second-order spatial accuracy for smooth solutions. Implicit stability permits large time steps, but those steps can still introduce unacceptable error.
Sources: src/heat_project/solvers.py and model.py; docs/engineering_derivation.md. Primary method reference: https://persson.berkeley.edu/math228b/html/finite_difference_methods_for_PDEs.html . Banded solver contract: https://docs.scipy.org/doc/scipy/reference/generated/scipy.linalg.solve_banded.html .

## Slide 3
Verification against exact solutions
Chart: Smooth spatial refinement
| 10 | 20 | 40 | 80
FTCS | 0.10629 | 0.026573 | 0.0065984 | 0.0016018
Backward Euler | 0.10641 | 0.026701 | 0.0067262 | 0.0017297
Two analytical checks
Smooth sine solution
Odd-sine cooling series
Reference crossing
1.649365 s
Spatial order ≈ 2
Time order ≈ 1
Smooth sine at t = 0.2 s. Fixed dt = 0.00001 s. Separate temporal check uses the exact semidiscrete mode.
Notes: Timing: 1:20–2:10.
Spoken explanation:
Verification starts with an exact sine solution that satisfies the boundary conditions from the beginning. A separate odd-sine series represents uniform cooling. Its converged centre crossing is 1.649365 seconds. The plotted refinement fixes the time step at ten to the minus five seconds and evaluates the smooth solution at point two seconds. The observed spatial orders approach two. A semidiscrete sine reference isolates temporal error, with observed order near one. Tests also check the tiny implicit system, boundaries, symmetry and input rejection. These checks verify the mathematical implementation. They do not establish measured physical accuracy.
Questions to anticipate: distinguish the compatible sine benchmark from the uniform initial condition. Explain the K-versus-2K series check and adaptive absolute tail bound. State that spatial time-halving changes are about 3.2e-5 degC. Explain why temporal comparison uses the exact semidiscrete eigenmode.
Sources: results/tables/spatial_convergence.csv, temporal_convergence.csv, smooth_verification.csv, reference_convergence.csv; results/summary.json; tests/ and reports/test_report.html. Verification versus physical validation: https://public.ksc.nasa.gov/mns/faq/ . Slab initial-boundary jump: https://doc.comsol.com/6.4/doc/com.comsol.help.models.heat.heat_conduction_in_slab/heat_conduction_in_slab.html . The native editable chart uses CSV-derived values rounded to 12 significant digits for Excel workbook portability. Canonical CSV evidence retains full precision.

## Slide 4
Method selection from measured evidence
Method | N | dt (s) | Max error (°C) | Crossing error (%) | Median (ms)
FTCS | 20 | 0.00625 | 0.589 | 0.229 | 2.873
Backward Euler | 40 | 0.00625 | 0.709 | 0.328 | 6.494
Selected: FTCS, N = 20, dt = 0.00625 s
Initial transfer case: 1.180 °C failure. Revised setting: fresh confirmation 0.552 °C, 0.214% crossing error.
Selected solve 11.65× faster than the fine baseline. Separate vectorisation check: 8.05×, identical output.
Notes: Timing: 2:10–3:00.
Spoken explanation:
The final selected setting uses twenty intervals and an explicit step of 0.00625 seconds. Its maximum benchmark error is 0.589 degrees, crossing error is 0.229 percent and median solver time is 2.873 milliseconds. The first faster choice failed a transfer case at 1.180 degrees. That failure became development evidence and prompted a stricter point eight degree development margin. The acceptance limit stayed at one degree. A fresh confirmation then reached 0.552 degrees and 0.214 percent crossing error without further tuning. This is selection within the measured candidate set on this machine.
Decision detail: original criteria were max field error <=1 degC at t=[0.1, 0.5, 1.0, 2.0, 3.0] s, crossing error <=2%, physical bounds and less than 1% crossing change on refinement. Selected refinement change 0.171801%. The initial baseline winner had only 0.006 degC margin and failed the first larger-temperature-span case. The added <=0.8 degC development margin is openly post hoc. The old case is reused development evidence. The final new case uses L=0.018 m, alpha=1.3e-5 m²/s, Ti=90, Tb=15, target=30 degC. It is a new mathematical check after revision, not experimental validation. Overall baseline-to-selected ratio 11.652324. Separate N=160 loop/vector equivalence has zero observed output difference and 8.053516 speedup.
Sources: results/summary.json and results/tables/candidate_comparison.csv, optimisation.csv. Timing protocol: warm solve, three independent batches, target batch duration at least 40 ms with a cap of 20 solves per batch, median per-solve times. Snapshot output, plotting, references and disk I/O excluded. Scalar maximum history remains. Results are environment-specific. Read summary design_revision, initial_confirmation and reused_case_development_check for the full revision history.

## Slide 5
Thickness and diffusivity sensitivity
Chart: Cooling time relative to baseline
| 0.5 | 1.0 | 2.0
Thickness L | 0.25 | 1 | 4
Diffusivity alpha | 2 | 1 | 0.5
t scales with L² / alpha
Double thickness
4 × cooling time
Double diffusivity
0.5 × cooling time
Analytical verification supports the model calculation. Real-process validation needs measured properties and boundary data.
Notes: Timing: 3:00–3:40.
Spoken explanation:
The sensitivity follows the heat equation's dimensionless time. Cooling time scales with thickness squared divided by diffusivity when the normalised target stays fixed. Doubling the thickness therefore multiplies the time by four. Doubling diffusivity halves it. The numerical ratios follow those predictions. The main physical limitation is the fixed face temperature. Real convection, contact resistance, lateral loss or changing properties could change the result. Independent measurements would be the next step before using the model for a real thermal process.
Sources: results/tables/sensitivity.csv and docs/engineering_derivation.md. Plotted values are numerical threshold time divided by the corresponding numerical baseline, rounded to 12 significant digits for portable editable workbook storage. Fixed Fourier number and target ratio make the scaling exact for the mathematical model. No empirical dataset is used.

## Slide 6
Repository demonstration and AI disclosure
Live walkthrough
README and reproducible commands
Source and generated API documentation
Tests, report and saved results
Genuine development history
Substantial AI contribution
Codex authored substantial code, tests, analysis and report drafts.
Student review and independent understanding remain essential.
The final setting meets the checked numerical targets. Real plate predictions still need experimental evidence.
Notes: Timing: 3:40–5:00.
Spoken explanation:
The repository contains reproducible commands, documented solvers, generated HTML, tests and saved evidence. Codex authored substantial code, tests, analysis and report drafts. The student remains responsible for reviewing the material and explaining the reasoning independently. The demonstration now follows one result from the README through the source documentation and test report, then shows the genuine repository history.
Repository walkthrough within the slide's 80 seconds: spend about 15 s on README, folders and one short command; about 20 s on generated API documentation and the actual FTCS update or BE boundary RHS; about 15 s on the final test report and one test's purpose; about 10 s on genuine Git history/actual hosted main branch if available; use the final 20 s for the selected result, model limit and AI disclosure. Keep windows prepared. A local folder does not itself demonstrate hosted GitHub access. Describe only personal review actually completed. If the hosted URL is not ready, state that directly.
Sources: README.md, docs/html/, reports/test_report.html, source and actual repository history; notes/ai_use_log.md. Original MMA3001 project brief pp. 6 and 9 requires disclosed AI use and unaided individual presentation/interview responses. No hosted URL or personal learning claim is invented here.